Town of Washington

### INLAND WETLANDS COMMISSION

WASHINGTON DEPOT, CT. 06794

To:  Inland Wetlands Commission

## From: Michael E. Ajello, WEO

Subject: WEO Activity Report, July 7, 2015

A summary of wetland related activities follows:

- Bee Brook Crossing – 23-30 Juniper Meadow Rd. – Pave (2) parking areas, Install (2) plunge pools – I received notification of the start of this work by S & S Paving on 6/16.  Grading of the south lot was begun on 6/26 and by 7/1 raised structures were in place on both parking lots.  At this time the north lot appears to be ready for asphalt and the south lot needs additional compacted base.

- Canal – 142 Sabbaday Lane – Pesticide Application – The pond was drained down slowly over the 4th of July weekend and treatment occurred on 7/6.  24 hrs. later all waters were still contained above the dam.

- The Gunnery – 22 South St. – Build (2) Soccer Fields – On July 1, I met with Bill Zekas of The Gunnery and Curt Smith of Smith & Co. Engineering to discuss minor modifications to the Soccer Field substrate designed to enhance and filter storm water infiltration into the field surface.  These additions involve the scarification of the compacted substrate and the addition of a layer of sand to promote absorption.  The plan has been reviewed by all involved parties including Land Tech Consultants, who fully support the concept.  I have asked that the new information be presented in written and mapped form for our meeting of 7/8/15 and I have given permission to proceed accordingly. A description of the plan is attached to this report for your perusal.

- Haight – 45 Old North Rd. – Demolish and rebuild dwelling, install pool – Framing is underway on this site.  The engineers have contacted me to report that the original underground electric service wires were buried directly with no conduit protection.  I’ve asked them to provide a revision request to the IWC specifying new conduits, their route, proposed sequences and supporting information for our July 8 meeting.  Erosion controls are in good condition at this time.

- Hamilton – 199 West Shore Rd. – Site re-development – Roadside drainage structures are being installed prior to excavating across West Shore Rd.  Rain gardens and sediment basins are being cleared and roughed out.  I have asked the contractors to: 1) Focus on stormwater control issues as late season inclement weather is a likely possibility and 2) clean up regularly around roadside catch basins for basically the same reasons.

- Hayes – 59 South Fenn Hill Rd. – Remove Invasive Species – Brush, undergrowth and invasive species were quickly cleared in the designated roadside area and the material was chipped right back into the same area.  Any suppressed growth should recover quickly.  This endeavor appears to be valueless but without negative wetland impact.

- Issavi – 27 West Shore Rd. – Veneer on concrete dock, rebuild stone wall –Approximately 15% of the dock veneer remains to be completed.  Jobsite conditions are clean and free of impact to the lake.

- Santangelo – 77 West Morris Rd. – Unauthorized deposition of materials –No additional activity has occurred on site since the deposition of materials near the watercourse.  The site appears to be deserted and my calls to these owners have gone unanswered.

- Sen – 116 Shearer Rd. – Unauthorized watercourse disruption – I have discussed this site with both contractors and landscapers and all are anticipating the submission of Brian Neff’s restoration plan so that the disrupted streambed can be recovered.

- Steep Rock Association – 147 Sabbaday Lane - Pedestrian Suspension Bridge – Concrete bridge footings were successfully placed on 6/25/15.  The site has been cleaned up and initial phases of the bridge construction are already underway.

- Stiles/Angiollo – 25 West Shore Rd. – Demolish and Re-place Dwelling – A low stone wall has been completed along the north property line but no recent construction activity has begun on site.

- Washington Montessori School – 240 Litchfield Tpk. – Parking area adjustments – The water quality basin on the east side of the Montessori access drive has been unchanged since it was cleared of vegetation late last year.  Approximately a third of the basin has been dredged at the inlet and a retaining dike of crushed stone functions as a pre-filter.  Additional filtration by the remaining cattails effectively traps any sediment from the stormwater before it transitions to the large sediment pond on the west side of the access drive.  Excavation work has begun on the soccer field and tennis court sites and all of that work is within the Town of Warren.  Some discoloration within the water quality basin is the only indication of disturbance on site as the drives and parking lots remain clear of mud or sedimentation.